## Slide 1
ITU-ML5G-PS-015: Network failure detection and root cause analysis in 5GC by NFV-based test environment
Team Kaien
2021-12-01
白石 善明 Yoshiaki SHIRAISHI
zenmei@port.kobe-u.ac.jp
阿部 海燕 Kaien ABE
abe@people.kobe-u.ac.jp
Team member:

## Slide 2
Project Introduction (1)
https://www.youtube.com/watch?v=T18ivePrIUQ

## Slide 3
Project Introduction (2)
https://www.youtube.com/watch?v=T18ivePrIUQ

## Slide 4
Data processing environment
計算機・ライブラ 環境
CPU/クロック周波数 | Intel(R) Core(TM) i7-9750H/2.60GHz
メモリー（Memory） | 32GB
OS | Ubuntu 18.04
Anacond3 (Environment) | Python3.8
json (process original json data） | csv (output data format)
Panadas (feature extraction) | sqlite（database for data post-processing
XGBoost (normal model) | XGBoost (increment model)
Computer configuration
Library
Original data is 77GB json file, it takes ３ days for feature extraction.
生データ(jsonファイル)は77GB, 特徴量抽出は３日頃かかります.

## Slide 5
Data investigation
8 types nodes are included in the dataset. we found failures are happened in 3 types nodes according to Failure label. In order to reduce calculation cost, only these 3 types nodes are processed. In reality scenario, all of nodes might be be processed.
amf | ○ 障害発生
ausf | ○ 障害発生
udm | ○ 障害発生
gnb | × 障害なし
smf | × 障害なし
upf | × 障害なし
nrf | × 障害なし
dn | × 障害なし
Nodes | Failure

## Slide 6
Failure label information
Notes: Failure parameter loss percent, failure parameter percentage, failure_parameter_stop_second,

## Slide 7
Data overview
Provided data: json files (77GB) | a Urban(都市) | c Rural(田舎) | b Middle(中間)
Train | 98,533 | 98,533 | 12,360
Test | 24,647 | 24,647 | 24,647
Failure label | 2480(train)+620(test) | 2480(train)+620(test) | 310(train)+620(test)
Train: (103 features) [nodes: amf, ausf, udm, respectively] | 295,599 (=98,533×3) (×103 特徴量) | 295,599 (=98,533×3) (×103 特徴量) | 37,080 (=12,360×3) (×103 特徴量)
Test: (103 features) [nodes: amf, ausf, udm, respectively] | 73,886 (≒24,647×3) (×103 特徴量) | 73,889 (≒24,647×3) (×103 特徴量) | 73,941 (=24,647×3) (×103 特徴量)
Abnormal data (from failure label) | 4,645 | 4,011 | 1,212
Abnormal /Total (%) | 13% | 10% | 10%
Extract features by python code
(One data is split to node data for more precisely label. Here node=3)
Table data of features (103)

## Slide 8
Data processing (1) データ分割のアイデア
Data_1 | amf | ausf | udm | Label=1
障害発生
(Failure)
障害なし
(No failure)
障害なし
(No Failure)
Positive
Data_1_amf | amf | Label=0
Data_1_ausf | ausf | Label=1
Data_1_udm | udm | Label=0
103 Features
103 Features
103 Features
103 Features
103 Features
103 Features
障害発生したノートを特定できる
Failure nodes can be located
Data is increased to 3 data

## Slide 9
Data processing (2)-how to select features
amf | 障害発生 | 204 (a,c) 154 (b)
ausf | 障害発生 | 175(a,c,b)
udm | 障害発生 | 177(a,c,b)
gnb | 障害なし | 
smf | 障害なし | 
upf | 障害なし | 
nrf | 障害なし | 
dn | 障害なし | 
Nodes | 障害 | 抽出項目数
In the provided dataset, failures happened in three nodes (total nodes=8) so that we only processing 3 nodes information for decreasing data processing work.
■Delete category info.
{interface_type,softwareloopback,tunnel,healthy,unknown
interface_name,
interface_if-index,
platform-fru-rp,
phys-address,
Healthy, critical, unknow,up, down,
Null…
}
■All of digital info.
e.g. memory-states,per-core-states,interface-parameter…
■Common features among all of nodes
特徴量の選抜基準
⇒ as features (103)

## Slide 10
Data processing (3)- how to label data
Form the failure data information (date,time,failure_type,node), we found the following features strongly related to failures, so that we labeled the training and test data according these features. There might be other features also related failures if we carry out furthermore data analysis.
Features 特徴量 | Abnormal 障害あり(label=1) | Normal 障害なし(label=0)
Memory_status： (148)(4512) software-oper_cisco-platform-software_control-processes_control-process_memory-stats_memory-status | 'Critical' 'Warning' | 'Healthy'
Minute_status_condition: 16 software-oper_cisco-platform-software_control-processes_control-process_load-avg-minutes_load-avg-minute_status_condition | 'Critical’ | 'Healthy'
Operation_status: 1(203)2(4996) interfaces_interfaces-state_interface_oper-status | 'down’ (start at, proc) (interface_down) | ‘up’
memory-stats_used-percent： software-oper_cisco-platform-software_control-processes_control-process_memory-stats_used-percent | >90% (memory_stress_stop) | <=90
software-oper_cisco-platform-software_control-processes_control-process_memory-stats_free-percent | <65 (memory_stress_stop) | >=65
software-oper_cisco-platform-software_control-processes_control-process_memory-stats_free-number | <250000 (memory_stress_stop) | >=250000
software-oper_cisco-platform-software_control-processes_control-process_per-core-stats_per-core-stat_idle | 0 (<0.5) (Bridge_delif) | >0.5
software-oper_cisco-platform-software_control-processes_control-process_per-core-stats_per-core-stat_nice | 0 (<0.5) (vcpu_overload_stop) | >0.5
正解ラベルの付け方
label
Verify by some features

## Slide 11
Feature Profile 1 （features name）

## Slide 12
Feature Profile (2)(values)

## Slide 13
Machine Learning by Xgboost 2-class model
Training by a (urban)： (Normal: 292,306; Abnormal: 3,293)
Test by c (rural)： (Normal: 73,082; Abnormal: 807)
Xgboost
100%
100%
100%
Recall
Precision
F-1
Best score
0
0(FP)
807(TP)
73,082
Confusion Matrix
Training by c (rural)： (Normal:292,395; Abnormal: 3,204)
Test by a (urban)： (Normal: 72,534; Abnormal: 1,352)
Xgboost
100%
100%
100%
Recall
Precision
F-1
Best score
0
0(FP)
1,352(TP)
72,534
Confusion Matrix
課程#1

## Slide 14
Increment Learning by data agumentation Ⅰ in XGB model
Xgboost
83%
100%
91%
Recall
Precision
F-1
135
0(FP)
677(TP)
73,129
Confusion Matrix
Trained model by a (urban)
◆ Trained model by a (urban) (Normal: 292,306; Abnormal: 3,293) + Training by b (middle)(Nomal:36,668; Abnormal: 412)
■ Test by b (middle)： (Normal: 73,129; Abnormal: 812)
Training by agumentation data b (middle)
課程#2

## Slide 15
Increment Learning by data agumentation Ⅰ in XGB model
Xgboost
100%
87%
93%
Recall
Precision
F-1
0
124(FP)
812(TP)
73,005
Confusion Matrix
Trained model by c (urban)
◆ Trained model by c (urban) (Normal: 292,306; Abnormal: 3,293) + Training by b (middle)(Nomal:36,668; Abnormal: 412)
■ Test by b (middle)： (Normal: 73,129; Abnormal: 812)
Training by agumentation data b (middle)
課程#2

## Slide 16
SHAP for Feature analysis (1)
障害原因分析
SHAPとはブラックボックスしがちな予測モデルの各変数の寄与率を求めるための手法で，各特徴量が予測モデルの結果に対して正負のどちらの方向に対してどれくらい寄与したかを把握することによって予測モデルの解釈を行えるようになります． SHAPの理論は主に協力ゲーム理論におけるShaply Valueが由来となっており，協力ゲーム理論におけるプレイヤーを特徴量に置き換えて特徴量毎の貢献度(Shapley Value)を求めています
Train in Rural (c)
Test in Urban (a)
The data distribution is different in rural (train)（ and urban (test) area, so that the features contributions (shap value) to detect abnormal are somewhat different.

## Slide 17
SHAP for Feature analysis (2)
障害原因分析
Train in urban (a)
Test in Rural (c)

## Slide 18
Improvement Proposal
改善点など
Feature clustering or mapping is helpful to confirm the feature’s effectiveness
Investigate the influence from different information (CPU load info, traffic info, five-g session info) separately by training 3 AI models respectively.
How to choose features should be investigate more deeply.